## Slide 1: Superscalar Processor Simulator
Finn Wilkinson – FW17231

## Slide 2: Architecture Design
Fetch
Decode
Issue
Execute
Write Back

## Slide 3: Processor Features
General
32 General Purpose Registers
5 stage pipeline
  Fetch, Decode, Issue, Execute, Write-Back
Multi-Cycle instructions
  Multiply - 2 cycles
  Divide - 16 cycles
Out-of-Order execution
Register re-naming
  Utilised Register Address Table
  Prevents Name Dependencies, WAW & WAR hazards
Scalar, 2-way superscalar, or 4-way superscalar
Pipeline Features
2 Arithmetic EUs
1 Branch and Logic EU
1 Load and Store EU
Grouped Reservation Stations
  16 spaces for Arithmetic
  8 spaces for Branch and Logic
  8 spaces for Load and Store
Result forwarding
Branch Prediction
Can select from
  Fixed – Always predicts branch is taken
  Static – If jumping backwards predict taken
  1-bit Dynamic – Make prediction on previous result
  2-bit Dynamic – Make prediction on previous 2 results
BTB keeps history of all branches seen before
  Also keeps track of previous results if dynamic prediction selected
Branch in Pipeline Buffer
  Tracks un-executed branches in the pipeline
  Ensures nothing is committed to ARF or MEM out of program order
  Allows for easy misprediction recovery and flushing
Memory and Write-Back
Variable size Re-Order Buffer (default is 128)
  Ensures program order write back to ARF, preventing RAW hazards
Load-Store Queue of size 128
  Ensures Loads and Stores happen in program order
  Loads wait for all previous store addresses to be known before being issued to prevent RAW hazards

## Slide 4: Benchmark Programs
All Scripts are looped in assembly 100 times to gain a more accurate IPC
Factorial | Recursively calculates the factorial of 12
Matrix Multiplication | Multiplies together a (6x4) matrix and a (4x6) matrix using branches to loop round
Unrolled Matrix Multiplication | Multiplies together a (6x4) matrix and a (4x6) matrix with an unrolled loop
Vector Addition | Adds together two vectors of length 10 A[i] = B[i] + c[i]
Quick Sort | Applies the quicksort algorithm to a list of length 30 utilising recursion and an in-memory stack
Game of Life | 20 iterations of Conway’s game of life on a 16x16 grid in-memory with wrap-around boarders

## Slide 5: Experiment #1 – Number of Pipelines
Hypothesis
Doubling the number of pipelines will increase the IPC by x2, as well as reducing the number of cycles taken to execute each script by half.
Experiment
Comparing IPC values and total cycles for 1, 2, and 4 pipelines over all benchmark programs. 2-bit Dynamic Branch prediction will be used as well as a 512-bit ROB to achieve as best results as possible for each test.
Results
We can see that from 1 to 2 pipelines the IPC is roughly doubled for each of the benchmarks. However from 2 to 4 pipelines, this IPC gain slows down to approximately 55%.
Similarly with the cycle count, from 1 to 2 pipelines we see a halving in the number of cycles each benchmark takes. Differently from the IPC measure however, with the exception of Vector Addition, increasing from 2 to 4 pipelines also sees another halving in how many cycles each benchmark takes.
Chart: IPC for Each Pipeline Count
| Factorial | Matrix Multiplication | Matrix Multiplication (Unrolled) | Vector Addition | Quick Sort | Game of Life
Scalar IPC | 0.96 | 0.99 | 1 | 0.97 | 0.95 | 0.97
2-Way IPC | 1.86 | 1.93 | 2 | 1.88 | 1.77 | 1.84
4-Way IPC | 3.11 | 3.68 | 3.89 | 2.14 | 3.16 | 3.33
Chart: Cycles for Each Pipeline Count
| Factorial | Matrix Multiplication | Matrix Multiplication (Unrolled) | Vector Addition | Quick Sort | Game of Life
Scalar Cycles | 5712 | 67456 | 61656 | 6648 | 459193 | 402273
2-Way Cycles | 3012 | 34682 | 30833 | 3528 | 250981 | 212589
4-Way Cycles | 1770 | 18149 | 15867 | 3017 | 143128 | 121819

## Slide 6: Experiment #2 – Comparing Branch Predictors
Hypothesis
For each of the benchmark programs, each successive branch prediction method will decrease the number of processor flushes required. With Fixed causing the most, then Static, 1-bit Dynamic, then 2-bit Dynamic with the fewest flushes.
Experiment
For a 4 pipeline processor with 512-bit ROB, test each branch prediction type and compare the number of flushes performed.
Results
Across the board we see varying results for each branch prediction type. For the first 4 benchmarks, all predictors a yield similar number of flushes which is most likely down to the nature of the programs themselves - mainly having unconditional and backwards jumping branches. This means that all our predictor types will predict taken, which more often than not is correct.
Our Game of Life benchmark yields our hypothesised result, probably due to its branches jumping forwards often, being mostly unconditional branches, and being variable whether they are taken or not.
Whilst the Quick Sort results may seem odd at first, it is the only script to use the JMP command, which takes a register value as the jump address. Furthermore, this jump is always a forward jump in this particular benchmark. Seeing as the Static predictor always predicts False for forward jumping branches, this explains the huge increase in the number of flushes required. The other branch predictor variants are very similar, such as the rest of the scripts.
Chart: Flush Count for Each Branch Prediction Type
| Factorial | Matrix Multiplication | Matrix Multiplication (Unrolled) | Vector Addition | Quick Sort | Game of Life
Fixed Flushes | 1201 | 501 | 1 | 101 | 11825 | 124945
Static Flushes | 102 | 501 | 1 | 101 | 57650 | 17025
1bitD Flushes | 207 | 999 | 1 | 200 | 11406 | 8064
2bitD Flushes | 102 | 501 | 1 | 101 | 11516 | 6895

## Slide 7: Experiment #3 – Size of Re-Order Buffer (ROB)
Hypothesis
An increased ROB size will increase the IPC and reduce the number of stalls and cycles.
Experiment
For a 4-way superscalar processor with 2-bit dynamic branch prediction, the ROB size will be increased from 8 to 512 in logical steps for all benchmark programs.
Results
As predicted, increasing the number of entries the ROB has also increases the IPC for the most part. From about 64 to 128 entries, we see the IPC level off, which tells us that the system is bottle-necked else where. This is most likely the size of the reservation stations in each pipeline, as if they are full then no instruction can be decoded and allocated a ROB position.
It could also be limited by the number of EUs inside each pipeline, however, it is unclear without testing how much performance could be gained, or how many more reservation station spaces or EUs would be needed to see a further increase in the IPC.
Chart: IPC for Different ROB sizes
| 8 | 16 | 32 | 64 | 128 | 256 | 512
Factorial | 1.89 | 2.2 | 2.79 | 3.11 | 3.11 | 3.11 | 3.11
Matrix Multiplication | 1.67 | 2.57 | 3.6 | 3.68 | 3.68 | 3.68 | 3.68
Matrix Multiplication (Unrolled) | 1.66 | 2.73 | 3.51 | 3.86 | 3.89 | 3.89 | 3.89
Vector Addition | 1.94 | 2.14 | 2.14 | 2.29 | 2.14 | 2.14 | 2.14
Quick Sort | 1.88 | 2.93 | 3.16 | 3.16 | 3.16 | 3.16 | 3.16
Game of Life | 2.13 | 3.14 | 3.33 | 3.33 | 3.33 | 3.33 | 3.33